## Slide 1: Support Vector Classification of Musical Instruments
Thomas Martin & Daniel Salazar
CSU East Bay
CMPE 344
Notes: Thomas and Daniel

## Slide 2: Project Overview
Goal: Develop a stand-alone platform built around the Beaglebone Black to record live music and classify the instrument that is playing in real time.
Instrument Classification: Machine learning model developed to classify the instrument being played.
Data Set: 5,438 audio samples of 7 instruments retrieved from the Philharmonia orchestra used to develop the machine learning model.
Hardware Components: Beaglebone Black, Microphone, 16x2 character LCD, push-button, and 3D printed case used to construct the project.
Notes: Daniel

## Slide 3: Feature Set
Project encompasses 7 features (instruments):
Cello (C2-C6)
  889 audio samples
Clarinet (E3-C7)
  846 audio samples
Guitar (E3-E6)
  106 audio samples
Saxophone (Bb3-G6)
  732 audio samples
Trumpet (F#3-D6)
  485 audio samples
Violin (G3-A7)
  1502 audio samples
Flute (C4-D7)
  878 audio samples
Notes: Thomas

## Slide 4: Machine Learning Workflow
Data Preprocessing
  Convert .mp3 files to .wav files
  Remove leading and trailing silence
Feature Extraction
  Compute MFCC values (Mel Frequency Cepstrum Coefficients) for each audio sample and append instrument labels
Model Training
  Support Vector Machine (SVM) model with RBF kernel
  75/25 train-test split
Model Testing
  93-97% accuracy with trained model on Philharmonia data
Model Persistence
  Final model saved to ‘pickle’ file to ensure classification consistency among tests
Notes: Thomas

## Slide 5: Machine Learning Model: SVM The Support Vector Machine (SVM ) finds a linear separating hyperplane with the maximal margin in this higher dimensional space. This Radial Basis Function (RBF) kernel nonlinearly maps samples into a higher dimensional space so it, unlike the linear kernel, can handle the case when the relation between class labels and attributes is nonlinear. There are some situations where the RBF kernel is not suitable. In particular, when the number of features is very large, one may just use the linear kernel.
Notes: Daniel

## Slide 6: SVM Model & Audio Results
93-97% combined accuracy with all instruments when using MFCC values extracted from source audio files
When using the microphone to record audio data classification accuracy varies based on instrument
  Instruments with a greater number of audio samples performed better
  Most recognized instrument: Clarinet
  Least recognized instrument: Guitar
Notes: Daniel

## Slide 7: Microphone and Audio Analysis
Audio spectrogram of trumpet clip (Mezzo Forte Tenuto) from Philharmonia dataset (source)
Audio spectrogram of the same trumpet clip captured using the Beaglebone and USB microphone
Notes: Thomas

## Slide 8: Hardware Results
16x2 LCD provided effective means to convey instructions and errors to user
  Simple potentiometer control for brightness
  Wire soldering and management not as simple as I2C option
AmazonBasics microphone was not able to record high-quality audio data
  Background noise readily audible
  Simple USB interface and easy to troubleshoot
Push button
  Controlling with Adafruit_BBIO.GPIO library was relatively straight-forward
3D printed case
  Housed all hardware components well
  10 hour print time
Notes: Daniel

## Slide 9: Improvement Opportunities
Hardware
  Higher quality microphone
  LCD with I2C backpack
  Portable power supply
Software
  Configure Python script to execute automatically upon system boot-up
Machine learning
  Use larger source audio dataset for each instrument
  Use the same number of audio samples for each instrument
  Try other classification algorithms (KNN, random forest, SVM with linear kernel)
  Train model with audio samples collected with the microphone used for eventual testing
  Train model to classify all instruments
Notes: Thomas and Daniel

## Slide 10: Summary
Developed a Beaglebone-based platform with a SVM machine learning model capable of classifying 7 different instruments from music recorded using a USB microphone
  Successfully created a stand-alone platform with a simple UI
High test accuracy achieved with source audio data
Test accuracy with USB audio data varied based on instrument
Improved test accuracy possible with changes to the audio hardware, machine learning model, and the source data set
Notes: Thomas

## Slide 11: Work Cited
Software Libraries
Scikit Learn - Support Vector Machines
  https://scikit-learn.org/stable/modules/svm.html
Librosa - Music and Audio Analysis
  https://librosa.github.io/librosa/index.html
Research Projects
Musical Instrument Classifiers
  https://github.com/ArushiSinghal/Automatic-Instrument-Identification
  https://github.com/IvyZX/music-instrument-classifier
Data Set
  http://www.philharmonia.co.uk/explore/sound_samples
3D Printed Devices
1602A LCD Case
  https://www.thingiverse.com/thing:1873666
Notes: Thomas and Daniel